## Slide 1: MPI + OpenMP
February 9th, 2018
Presenters:
Barbara Chapman
Oscar Hernandez
Martin Kong

## Slide 2: DOE’s Office of Science Computation User Facilities
DOE is leader in open High-Performance Computing
Provide the world’s most powerful computational tools for open science
Access is free to researchers who publish
Boost US competitiveness
Attract the best and brightest researchers
NERSC
Edison is 2.57 PF
OLCF
Titan is 27 PF
ALCF
Mira is 10 PF
Notes: DOE is leader in HPC
8 of 14 fastest computers in the world
EVERY US #1 computer has been at a DOE laboratory

## Slide 3: Roadmap to Exascale (ORNL)
CORAL System
Since clock-rate scaling ended in 2003, HPC performance has been achieved through increased parallelism. Jaguar scaled to 300,000 CPU cores. | Titan and beyond deliver hierarchical parallelism with very powerful nodes. MPI plus thread level parallelism through OpenMP or OpenACC plus vectors
Jaguar: 2.3 PF
Multi-core CPU
7 MW
Titan: 27 PF
Hybrid GPU/CPU
9 MW
2010
2012
2017
2022
OLCF5: 5-10x Summit
~20 MW
Summit: 5-10x Titan
Hybrid GPU/CPU
10 MW

## Slide 4: Two Architecture Paths for Today and Future Leadership Systems
Heterogeneous Systems (e.g. Titan, Summit)
CPU(s) / GPU(s)
Likely to have multiple CPUs and GPUs per node
Small number of very powerful nodes
Expect data movement issues to be much easier than previous systems – coherent shared memory within a node
Multiple levels of memory – on package, DDR, and non-volatile
Homogenous (e.g. Sequoia/Mira)
10’s of thousands of nodes with millions of cores
Homogeneous cores
Multiple levels of memory – on package, DDR, and non-volatile
Unlike prior generations, future products are likely to be self hosted
Power concerns for large supercomputers are driving the largest systems to either Heterogeneous or Homogenous (manycore) architectures

## Slide 5
We need to redo this slide

## Slide 6: Programming Model: MPI + OpenMP
Efficient programming for clusters of shared memory nodes
Hierarchical system layout
  Parallelism across nodes, within node (threads, simd, accelerators)
Hybrid programming
  MPI between nodes
  Shared memory programming inside the node
    OpenMP
    MPI-3 shared memory
    Accelerator support in OpenMP

## Slide 7: MPI and OpenMP
Pure MPI Pro
  Portable to distributed and shared memory machines
  Scales beyond one node
  No data placement problem
Pure MPI Cons
  Difficult to developed and debug
  High latency, low bandwidth
  Explicit communication
  Large granularity
  Difficult load balancing
Pure OpenMP pros
  Easy to implement parallelism
  Low latency, high bandwidth
  Implicit communication
  Coarse and fine granularity
  Dynamic load balancing
Pure OpenMP Cons
  Only on shared memory systems
  Scale within one node
  Possibly data locality problem
  No specific thread order

## Slide 8: Why Hybrid MPI + OpenMP?
Homogenous and Heterogeneous systems have large core counts per node
  Cori: Xeon Phi (KNL) – Total of 240 threads per node
  Summit: Total 176 (SMT4) Power9 threads + 6 Volta GPUs per node
Application likely to run with MPI but not with good performance
  Needs hybrid programming to manage threading, improve SIMD, accelerator programming
Many applications will not fit into the node memory using Pure MPI (e.g. per core) because of the memory overhead for each MPI task
Hybrid MPI/OpenMP is the recommended programming model to achieve scaling capability and code portability, new trend
Incremental parallelism with OpenMP for cores and accelerators
Avoids extra communication overhead within the node
Improves load-balancing across MPI tasks

## Slide 9: Choices for Programming models
Pure MPI (one MPI process on each core)
Hybrid: MPI + X
  Shared memory (OpenMP)
  Accelerator programming (OpenMP 4.5 shared memory + offload, CUDA, etc)
Other
  MPI message passing + MPI shared memory
  PGAS: UPC/UPC++, CAF, GA, etc
  Runtime tasks
MPI + OpenMP tend to be slower than pure MPI
  Why? Many factors affect this

## Slide 10: Hybrid MPI+OpenMP Programming Styles
MPI
MPI + OpenMP
Hybrid MPI +
MPI-3 (Shared Memory)
OpenMP Only
No overlap of Communication and Computation
Overlapping Communication and Communication
Master only
(outside omp parallel regions)
Single Thread call MPI
(inside omp parallel region)
All threads call MPI
(inside omp parallel region)
Offload to Accelerator(s) – (if available)
(e.g. OpenMP target regions, CUDA)

## Slide 11: Need slides on OpenMP affinity (Based on Aachen slides)
Introduce concept of OMP_PLACES, OMP_PROC_BIND and NUM_THREADS
Introduce concept of nested parallelism and OMP_PLACES

## Slide 12: Summit – MPI+OpenMP Affinity
Use jsrun to launch MPI, MPI+OpenMP, OpenMP (only) applications
MPI+OpenMP affinity set by jsrun
  MPI task placement
  Sets OpenMP places ICV and environment variable
  OpenMP thread affinity controlled by OMP_PROC_BIND
mpirun is also available (not preferred)
For more information on jsrun:
  https://beta.olcf.ornl.gov/for-users/system-user-guides/summit/running-jobs/

## Slide 13: JSRUN – Resource Sets to control MPI+OpenMP affinity
A resource set
  Controls how resources are managed within the node
  Can create one ore more resource sets within a node
  Each resource set contain 1 or more cores and 0 or more GPUs
Understand how the application interacts with the system
  How many tasks/threads per GPU
  Does each task expect to see a single GPU? (or multiple GPUs)
Create resource sets to specify:
  GPUs per resource set
  Cores per resource set
  MPI tasks per resource set
    Distribution
Decide the # of resource set needed in applications

## Slide 14: Resources available in a Summit Node
A Summit Node: cores, hardware threads and GPUs
GPU
GPU
GPU
GPU
GPU
GPU
POWER 9
POWER 9
Hardware Characteristics
2 POWER9 per node
22 cores per P9
4 hardware threads per core
6 Volta GPUs connected NVLINK2
Node Configuration:
2 cores reserved for OS
Applications will have 42 cores;
168 threads hardware threads
7 cores per GPU; 28 hw threads
per GPU
Core
Hardware thread (SMT4)

## Slide 15: Resources sets in Summit Node
A Summit Node: cores, hardware threads and GPUs
GPU
GPU
GPU
GPU
GPU
GPU
POWER 9
POWER 9
Resource Set (example)
1 GPU
7 cores per P9
(28 Hardware Threads (SMT4))
Node resources
A node can have up to 6 resource sets of this type
MPI tasks are distributed across resource sets. Example:
1 MPI task per resource set
2 MPI tasks per resource set
Or with other distributions (cyclic)
Core
Hardware thread (SMT4)
A resource set

## Slide 16: Example of MPI+OpenMP Affinity (E3SM)
2 MPI task per GPU and 7 OpenMP threads (hw threads – SMT2).
  2 MPI task access a GPU
GPU
GPU
GPU
GPU
GPU
GPU
POWER 9
POWER 9
OS
OS
MPI Task
OpenMP thread
NVIDIA Volta GPUs

## Slide 17: Example of MPI+OpenMP Affinity (Dirac, GTC, HACC, NWCHEM)
1 MPI task per GPU and 28 OpenMP threads (hw threads – SMT4).
  1 MPI task per GPU
GPU
GPU
GPU
GPU
GPU
GPU
POWER 9
POWER 9
OS
OS
MPI Task
OpenMP thread
NVIDIA Volta GPUs

## Slide 18: Example of MPI+OpenMP Affinity (QMCPack)
1 MPI task per GPU and 7 OpenMP threads (cores).
  All MPI tasks access all GPUs (MPS)
GPU
GPU
GPU
GPU
GPU
GPU
POWER 9
POWER 9
OS
OS
MPI Task
OpenMP thread
NVIDIA Volta GPUs
All MPI Tasks Access all GPUs

## Slide 19: MPI+OpenMP: Affinity (LS-Dalton) / Tasking
1 MPI task per node and 42 OpenMP threads (cores).
  One MPI task access all GPUs
GPU
GPU
GPU
GPU
GPU
GPU
POWER 9
POWER 9
OS
OS
MPI Task
OpenMP thread
NVIDIA Volta GPUs
1 MPI Task Access all GPUs

## Slide 20: Example of MPI+OpenMP Affinity (NAMD)
10 MPI task per 3 GPU and 8 OpenMP threads (hw threads – SMT4).
  10 MPI tasks access 3 GPU (MPS)
GPU
GPU
GPU
GPU
GPU
GPU
POWER 9
POWER 9
OS
OS
MPI Task
OpenMP thread
NVIDIA Volta GPUs
3 GPUs
3 GPUs

## Slide 21: Overview: OpenMP 4.5 Update
Released at SC’15
Many refinements to device support
Clarifications and minor enhancements, including:
  Reductions for C/C++ arrays
  Runtime routines to support cancelation and affinity
Some new features have been added
  Support for doacross loops
  Divide loop into tasks with taskloop construct

## Slide 22: OpenMP 4.5 substantially improves device support
Unstructured data mapping
Asynchronous execution
Scalar variables are firstprivate by default
Device runtime routines: allocation, copy, etc.
Clauses to support device pointers
Ability to map structure elements
New combined constructs
New way to map global variables (link)

## Slide 23: OpenMP 4.5 has many other refinements to recent additions
Many clarifications and minor enhancements
  SIMD extensions
    SIMD and SIMD parallel loop chunk size control
  Addition of schedule modifiers: simd, monotonic, nonmonotonic
  Clarifications of thread affinity policies
  Grammar for OMP_PLACES
  Support for if clause on combined/composite constructs
Hints for locks and critical sections
Continues to increase Fortran 2003 support
  Ten limitations remain until 5.0
Task priorities
Improved support for C++ reference types
Compiler support: http://www.openmp.org/resources/openmp-compilers/

## Slide 24: OpenMP 5.0 Preview -- TR4 released November 2016
Major new feature is performance tool support (TR2+)
Some significant extensions to existing functionality
  Support for task reductions, including on taskloop construct
  Implicit declare target directives and other verbosity reducing changes
Many clarifications and minor enhancements, including:
  Use of any C/C++ lvalue in depend clauses
  Addition of depend clause to taskwait construct
  Addition of conditional modifier to lastprivate clause
  Permits declare target on C++ classes with virtual members
  Clarification of declare target C++ initializations

## Slide 25: OpenMP 5.0 will significantly extend TR4 & TR5
Main Topics for 5.0
  Memory locality, affinity and working with complex memory hierarchies
  Updates to support latest C/C++ standards, completion of Fortran 2003
  Continued improvements to device support and tasking, including:
    Deep copy for mapped variables; Improved support for multiple devices
    Unshackled threads, major extensions for task dependences
  Interoperability and composability
  Debugging tools support
OpenMP 5.0 is scheduled to be released by SC18
  TR6 (TBD – SC’17) will document most additions for 5.0

## Slide 26: Memory Management --- TR5 released November 2016
Language features for managing memory on systems with heterogeneous memories.
Main Concepts:
  Memory Spaces --- Represents memory resources
  Memory Traits --- {Location, Distance, Bandwidth, Latency, Persistence, etc}
  Allocator Traits
  Allocator and Directives APIs

## Slide 27: Help us shape the future of OpenMP
Connect with the SOLLVE project --- WBS# 1.3.1.15
  Complete our survey on the confluence site!
  Application engagement via shared milestones for FY17,18,19
OpenMP continues to grow
  28 members currently
You can contribute to our now planned annual TR or complete specification releases
Attend IWOMP, become a cOMPunity member
Become a member in the OpenMP ARB
  OpenMP membership types will become more accessible
  Please let us know if you would be interested

## Slide 28: OpenMP 4.5 target
Wednesday, June 28th , 2017
Presenters:
Tom Scogland
Oscar Hernandez
Credits for some of the material
IWOMP 2016 tutorial – James Beyer, Bronis de Supinski
OpenMP 4.5 Relevant Accelerator Features – Alexandre Eichenberger
OpenMP 4.5 Seminar – Tom Scogland

## Slide 29: OpenMP 4.0/4.5 – Accelerator model
OpenMP 4.0/4.5 supports heterogeneous systems (accelerators/devices)
Accelerator model
  One host device and
  One or more target devices
GPU(s)
Xeon Phi(s) –
(Accelerator and self-hosted)
Host Device
(CPU Multicore)
Single device attached
Multiple devices attached
With attached accelerator(s)

## Slide 30: OpenMP Target
Device:
  An implementation-defined (logical) execution unit (or accelerator)
Device data environment
  Storage associated with the device
The execution model is host-centric (or initial device)
  Host creates/destroys data environment on device(s)
  Host maps data to the device(s) data environment
  Host offloads OpenMP target regions to target device(s)
  Host updates the data between the host and device(s)

## Slide 31: OpenMP 4.5 Device Constructs
Execute code on a target device
  omp target [clause[[,] clause],…]
  structured-block
  omp declare target
  [function-definitions-or-declarations]
Manage the device data environment
  map ([map-type:] list)
  map-type := alloc | tofrom | to | from | release | delete
  omp target data [clause[[,] clause], …]
  structured-block
  omp target enter/exit data [clause[[,] clause], …]
  omp target update [clause[[,] clause],…]
  omp declare target
  [variable-definitions-or-declarations]
Parallelism & Workshare for devices
  omp teams [clause[[,] clause],…]
  structured-block
  omp distribute [clause[[,] clause],…]
  for-loops
Device Runtime Support
  void omp_set_default_device(int dev_num)
  int omp_get_default_device(void)
  int omp_get _num_devices(void)
  int omp_get_team_num(void)
  int omp_is_initial_device(void)
  …
Environment variables
  OMP_DEFAULT_DEVICE
  OMP_THREAD_LIMIT

## Slide 32: OpenMP target example
..
!$omp target map(to:u) map(from:uold)
!$omp parallel do collapse(2)
do j=1,m
do i=1,n
uold(i,j) = u(i,j)
enddo
enddo
!$omp end target
..
An example of OpenMP 4.5 for accelerators
Device
initialize device
allocates: u, uold on device data environment
copies in: u
copies out: uold
deallocates: u, uold
host thread
host thread
barrier
Execute target
code
!$omp parallel do
initial device thread
Executed on
the device
Use target construct to:
Transfer control from the host to the target device
Map variables to/from the device data environment
Host thread waits until target region completes
Use nowait for asynchronous execution

## Slide 33: OpenMP Target and Data Regions
The map clauses determine how an original (initial device) variable in a data environment is mapped to a corresponding variable in a device data environment
  Mapped variable:
    An original variable in a (host) data environment has a corresponding variable in a device data environment
  Mapped type:
    A type that is amenable for mapped variables
    Bitwise copy-able plus additional restrictions
Host Data Environment
Variables
Device Data Environment
Device Data Environment
Device(s) Data Environment
Device Mapped
Variables

## Slide 34: League and teams of threads
League
  Set of thread teams created by a teams construct
Contention group
  Threads of a team in a league and their descendant threads
  Threads can synchronize in the same contention group
#pragma omp teams
#pragma omp parallel
League
team
// creates N teams of size 1
Contention Group
#pragma omp target
// creates initial target thread
// creates M threads within a team

## Slide 35: teams construct
The teams construct creates a league of thread teams
  The master threads of all teams executes the team region
  The number of teams is specified by the num_teams clause
  Each team executes with thread_limit threads
  Threads in different teams cannot synchronize with each other
  Must be perfectly nested in a target construct
    No statements or directives between teams and target constructs
  Only special openmp constructs can be nested inside a teams construct
    distribute
    parallel
    parallel for
    parallel sections

## Slide 36: distribute construct
Work-sharing construct for target and teams regions
  Distribute the iterations of a loop across the master threads of the teams executing the region
  No implicit barrier at the end of the construct
dist_schedule(kind[, chunk_size])
  kind must be static scheduling
  Chunks are distribute in round-robing fashion with chunk_size
  Each team receives at least one evenly distributed chunk (if no chunk_size is specified)
#pragma omp target map(tofrom: A)
#pragma omp teams
#pragma omp distribute
for (i=0; i< N; i ++)
A[i] = ….

## Slide 37: Writing Portable Device code
#pragma omp target map(tofrom: A)
#pragma omp teams distribute parallel for simd collapse(3) // combined directive
for(i=0; i<N; i++)
for(j=0; j<N; j++)
for(k=0; k<N; k++)
A[i][j][k] = ….
Use OpenMP 4 “Accelerator Model” to target multiple architectures:
GPUs, Intel Xeon Phi, and multicore CPUs, etc.
Make your OpenMP adaptable or using defaults for:
  # of teams,
  dist_schedule,
  thread_limit #,
  # of threads in parallel regions,
  parallel for loop schedules,
  SIMD length
Example:
Xeon Phi implementation may chose num_teams(1), thread_limit(1) and simdlen(V)
GPUs implementation may chose num_teams(N), thread_limit(M) and simdlen(V)

## Slide 38: Questions?